Interior Dome Antenna for Repeater Systems

CM222

Specifications:

| Model | CM222 |
| --- | --- |
| Frequency Range (MHz) | 806-960, 1710-2500 |
| Gain (dBi) | 3 |
| VSWR | < 1.5 |
| Beamwidth (degrees) | 360 |
| Impedance (ohms) | 50 |
| Polarization | Vertical |
| Max Power (W) | 50 |
| Connector Type | N/Female |
| Dimension (mm) | 186 (diameter) x 80 (height) |
| Weight (kg) | 0.49 |
| Color | White |

Installation:

- Drill hole (approximately 18 to 20mm in diameter) in ceiling. Ceiling depth can be up to approximately 1.25”.

- Insert hollow mount pole of antenna through hole in ceiling and tighten plastic nut.